## Slide 1: DEEP MIMO DETECTION
THANOPOULOU KONSTANTINA
1066581 SMHN

## Slide 2: MIMO Detection Problem
System Model:
Received signal: y = H*x + n (flat fading channel)
H ∈​: Channel matrix
x ∈ : Transmitted symbol vector (QPSK)
n: Additive white Gaussian noise (AWGN),
where:
Goal:
Estimate x from y given H.
Notes: 4*8 MIMO

## Slide 3: Block Diagram

## Slide 4: LMMSE detection flow
(1) Random Bit Generation & Mapping to QPSK symbols & normalization
(2) Pass the symbols through a flat-fading channel ‐ Create a random complex channel H matrix ‐ Add AWGN noise
(3) Pass the received signal y and the channel H to the LMMSE equalizer (to get x_hat)
(4) Get the llr from the demapper used on x_hat
(5) Get the bits of the symbol x_hat by performing hard decision given the llr
(6) Compare the bits detected with the ground truth bits to get bit error rate (BER)

## Slide 5: DetNet detection flow
Random Bit Generation & Mapping to QPSK symbols & normalization
Pass the symbols through a flat-fading channel
- Create a random complex channel H matrix
- Add AWGN noise
(3) Real-Valued Conversion to enter values to DetNet detector
(4) Pass the real-valued channel and received signal to the DetNet model (inference).
(5) Turn the estimated x value (x_hat) from real to complex.
(6) Get the llr from the demapper used on x_hat
(7) Get the bits of the symbol x_hat by performing hard decision given the llr.
(8) Compare the bits detected with the ground truth bits to get bit error rate (BER).

## Slide 6: LMMSE Detector – Number of operations
Mathematical Expression:
=
Compute Hermitian Transpose: (Size: ×
(2) Compute Gram Matrix: (Size: × ​)
(3) Add regularization: (Size: × ​)
(4) Invert the matrix: (Size: × ​)
(5) Multiply matrix with vector y: (Size:
(6) Multiply (4) with (5) →
Number of approximate operations (flops):
(Each complex multiply is treated as ∼4 flops, and each complex add is ∼2 flops)
×
6 - 2
(only affects diagonal elements)
(6 - 2)
6 - 2

## Slide 7: DetNet Detector – Compute Initial ZF estimate
Mathematical Expression:
= (zero-forcing initialization – ZF)
Compute Hermitian Transpose: (Size: ×
(2) Compute Gram Matrix: (Size: × ​)
(3) Invert the matrix: (Size: × ​)
(4) Multiply matrix with vector y: (Size:
(5) Multiply (3) with (4) →
Number of approximate operations (flops):
(Each complex multiply is treated as ∼4 flops, and each complex add is ∼2 flops)
×
6 - 2
(6 - 2)
6 - 2

## Slide 8: DetNet Detector – Compute
Mathematical Expression:
= ,
(precomputed , )
Iterate through L layers, in each one:
(1) Compute (Size:
(2) Dense layer computation: Wz+b (Size: 2 × 1)
where W (Size: 2 × 6)
In each neuron (takes a row from W):
(i) Vector x vector: W * z (Size: 1)
(ii) Bias addition (Size: 1)
(iii) Activation function: f(x)=−1+
Number of approximate operations (flops):
(Each complex multiply is treated as ∼4 flops, and each complex add is ∼2 flops)
8 - 2
(i) 12 -1
(ii) 1
(iii) 18 (each division ~6flops)
Total flops per neuron: 12 18
Total flops per layer: (12 18) 2=
= 24 + 36
Total flops for L layers: L (24 + 36 )
(L=10 in our case)
Note: H=
Notes: All are converted in real domain inside the DNN, so the dimensions are double the original size

## Slide 9: Training
Training Hyperparameters:
Number of Epochs: 50
Steps per Epoch: 150
Batch Size: 2000 per step
Optimizer: Adam with learning rate 0.001
Loss & Regularization:
Per‐layer MSE with a logarithmic weight: log(i) for layer i
SNR Scheduling
First 25 epochs: SNR sampled uniformly between [0,5] dB
Then in the next 25 epochs between [6,10] dB

## Slide 10: Simulation setup
System Parameters
=4
=8
QPSK modulation (2 bits/symbol)
SNR range: 0 to 10 dB with 0.5 dB step
Large batch size (100.000) to estimate BER reliably
QPSK symbols are normalized by
Noise Generation
AWGN with variance =

## Slide 11: RESULTS

## Slide 12: CONCLUSIONS
DetNet provides better BER performance than LMMSE at all SNR levels, despite its higher computational cost.
DetNet requires additional training and implementation complexity, whereas LMMSE is a linear detector with a closed-form solution and no training needed.
DetNet’s scalability is limited by its ZF initialization, which includes a matrix inversion similar to LMMSE. If a more efficient initialization were used, DetNet could scale better for larger MIMO systems.

## Slide 13: THANK YOU!
DetNet inspired by:
https://github.com/hello-zhanghao/MIMO_detection_algorithms/blob/master/DetNet.py